## Slide 1
Eutrophication: a major issue

## Slide 2: 1. Introduction to Eutrophication
Eutrophication: the process of becoming or being made eutrophic
Eutrophic: the state of being enriched in nutrients or food sources
In aquatic ecosystems, eutrophication is caused by
excessive inputs of nutrients. The nutrients enhance
algal growth, and this, in turn, may have a cascade of
effects on the ecosystem. These effects may
include: algal blooms, growth of undesirable algal
species, oxygen depletion or anoxia in bottom
waters, loss of cold-water fish species, abundance of
fish kills, unpleasant tastes and odors.

## Slide 3: 2. History
Eutrophication was recognized as a pollution problem in European and North American lakes and reservoirs in the mid- 20th century (Rohde, 1969).
Surveys showed that 54% of lakes in Asia; 53% in Europe, 48% in North America, 41% in South America and 28% in Africa are eutrophic (ILEC/Lake Biwa Research Institute, 1988-1993).

## Slide 4: 3. Identifying causes
Liebig’s Law: under steady state conditions, the growth of an organism is dependent on the amount of essential material that is available in least supply
Limiting nutrient: The one in shortest supply relative to demand. If you add more of that nutrient the plants/algae will grow
Phosphorus Nitrogen
freshwater salt & brackish

## Slide 5: Schindler’s (1974) study gave most compelling evidence for phosphorus being the cause of man-made eutrophication
Legislation was later adopted limiting P in detergents and effluents
fertilized with P, N and C
Basin fertilized with only C and N
Oligotrophic Experimental Lake 226, NW Ontario (after 2 months)

## Slide 7: 4. Process of Eutrophication
Oligotrophic lake with a low level of nutrients.
Artificial input of nutrients from
run-off and discharge of effluent.
Eutrophic lake with a high level
rapid algal growth decrease in DO
1 2
3
4

## Slide 8
Turbidity (cloudiness) of water increases as does rate of sedimentation.
Increased growth of rooted plants such as reeds.
Algal blooms during the Summer months
Development of anoxic conditions and release of noxious gases such as hydrogen sulphide, thioalcohols and ammonia
5
6
7
8

## Slide 9: 5. Sources of nutrient runoff

## Slide 10: 6. Effects
Thick algal blooms decrease sunlight penetration,
leads to death of submerged aquatic vegetation (less fish/shellfish habitat)
More organic matter leads to decrease of dissolved oxygen (DO) concentrations
CH2O + O2 = CO2 + H2O
  BOD = biological oxygen demand, a measure of how much O2 a given quantity of organic matter can remove from the water
  BOD: sewage = 165mg/L; food = 750mg/L; paper = 375mg/L
Anoxia kills fish (Healthy water has 8mg/L O2, fish die at 2mg/L)
  O2 sag curve

## Slide 11: O2 Sag Curve

## Slide 12
TOXIC ALGAE
– Addition of limiting nutrient (N, P), e.g. by excess fertilizer or sewage effluent can stimulate growth of certain cyanobacteria or dinoflagellates
Pfiesteria

## Slide 13: Algal Blooms “Red Tides” Very fast growth of algae leads to “bloom” or dense patches near water surface- “Red tide”: pigment of phytoplankton makes water appear discolored (can be red, green, brown, orange)

## Slide 14: Lake Erie: The Eutrophication Story
•
•
•
12th Largest lake in the world Detroit River from Lake Superior, Michigan, Huron and represents
~95% of current inflow Outflow: Niagara River to Lake Ontario

## Slide 15: The Source Problem- Phosphorus
Sewage and Industrial Waste
  Introduction of phosphorus-based detergents.
  9 million municipal population
  2 million septic tanks population
Agricultural Activity - Both Canada and US
  Drainage vast coastal wetlands
  Increased sediment runoff from tilled lands
  Increase phosphorus and nitrogen based fertilizer use

## Slide 16: The Solution
International Joint Commission (IJC) determined that eutrophication was occurring as a result of the high phosphorus loading entering the lake in the 1950 and 1960s.
$7.5 Billion spent since 1972 to bring into compliance with 1.0 mg/L phosphorus abatement program.
Goal is 11,000 metric tons/year phosphorus
Reduce the phosphorus in household detergents.

## Slide 17: 6. Prevention and Control Prevention:
Effectiveness
Sources of nutrients must be identified and evaluated, and then cost-effective methods of controls must be implemented.
Minimizing nonpoint pollution
The following steps are recommended to minimize the amount of pollution that can enter aquatic ecosystems from ambiguous sources;

## Slide 18
i. Riparian buffer zones
created
near
Riparian buffer zones can be waterways in an attempt to filter
pollutants; sediments
and nutrients are deposited here instead of
in water.
ii. Prevention policy
Laws regulating the discharge and treatment of sewage can led to dramatic nutrient reductions to surrounding ecosystems .

## Slide 19: contd…
iii. Nitrogen testing and modeling
Soil Nitrogen Testing (N-Testing) is a technique that helps farmers optimize the amount of fertilizer applied to crops.
By testing the soil and modeling the bare minimum amount of fertilizer needed, farmers reap economic benefits while the environment remains clean.

## Slide 20: Control:
1. Within-lake actions
Reduce mineralization
  Remove organic P before it is mineralized;
    Dredging
    Macrophyte harvesting

## Slide 21: Contd..
Reduce transport of inorg. P to epilimnion
  Hypolimnetic water withdrawal
Reduce P release from sediments
  Hypolimnetic aeration
P release from sediments is greatly enhanced by anoxic conditions under which iron oxides dissolve and release all P sorbed to their surfaces

## Slide 22: Lake aeration

## Slide 23: 8. Conclusion
“When you can’t breathe, nothing else matters”
decomposition
O2
Save us!