## Slide 1
STATISTICAL QUALITY CONTROL - II

## Slide 2: CONTROL CHATS FOR
constructed for controlling the variations in the average quality standard of the products in a production process.
R-CHART-: This chart is constructed for controlling the variations in the dispersion or variability of the quality standards of the products in a production process.
VARIABLES

V CHART/ MEAN CHART-: This chart is


## Slide 3: EXAMPLE-:
1 | 1 | 15 10 11 14
2 | 2 | 18 10 8 22
3 | 3 | 19 17 10 13
4 | 4 | 12 19 14 20
5 | 20 | 19 26 12 23
Sample No. Weights
Conversion factors for n=5, A2 =0.577, D3 =0, D4=2.115

## Slide 4: Solution-:
10
14
11
8
14
ΣR=57
14
14
16
16
20
Σ Σ =80
70
70
80
80
100
20 15 10 11 14
12 18 10 8 22
21 19 17 10 13
15 12 19 14 20
20 19 26 12 23
1
2
3
4
5
K=5
Range R=(L-S)
R =(ΣX/
5)
Total
Weights (ΣX)
Sample Weights (X) no.

## Slide 5: Grand4i
= ΣΣ /K = 80/5=16
Grand Grand
Chart
= 16 (Central line)
Control limits-:
2
UCL = Grandl + A 2
= 16 + 0.577 x 11.4
= 22.577
LCL = Grand7 - A2
= 16 – 0.577 x 11.4
= 9.423

## Slide 6: <= ΣR/K = 57/5 = 11.4
Range Chart
R = 11.4 (Central line)
Control limits-:
44
UCL = D . L
= 2.115 x 11.4
= 24.09
LCL = D3. C
= 0 x 11.4
= 0

## Slide 7
σ Chart-: This chart is constructed to get a better picture of the variations in the quality standard in a process than that is obtained from the range chart provided the standard deviation(σ) of the various samples are readily available.
Example-: Quality control is maintained in a factory with the help of standard deviation chart. Ten items are chosen in every sample. 18 samples in all were chosen whose ΣS was
8.28. Determine the three sigma limits of σ- chart. You may use the following-:
n = 10, B3 = 0.28, B4 = 1.72, K = 18.
Solution-:
= ΣS/K = 8.28/18 = 0.46 Σ
4
UCL = B . L
3
LCL = B . L
= 1.72 x 0.46
= 0.28 x 0.46
= 0.7912
= 0.1288

## Slide 8: Control Charts for Attributes-:
p-chart-: This chart is constructed for controlling

the quality standard in the average fraction defective of the products in a process when the observed sample items are classified into defectives & non- defectives.
np-chart-: This chart is constructed for controlling
the quality standard of attributes in a process where the sample size is equal & it is required to plot the no. of defectives (np) in samples instead of fraction defectives (p).

## Slide 9: Example-:
Σd = 60
K = 10
0.05
0.03
0.03
0.06
0.05
0.06
0.08
0.1
0.1
0.04
5
3
3
6
5
6
8
10
10
4
100
100
100
100
100
100
100
100
100
100
1
2
3
4
5
6
7
8
9
10
Fraction
defectives (d/n)
No. of
defectives (d)
Size of sample
(n)
Sample No.

## Slide 10: otal no. of units =
= Total no. of defectives/T
60/1000 = 0.06
»q̅̅ = 1- = 1- 0.06 = 0.94
= 0.06 (central line) UCL = C + 3√ √ . q̅//n
= 0.06 + 3√0.06x0.94/100
= 0.1311
LCL = L - 3 √ √ . q̅//n
= 0.06 - 3 √ 0.06x0.94/100
= -0.0111 = 0

## Slide 12: Example-:
An inspection of 10 samples of size 400 ea
ch from 10 lo
ts reveal
the following number of defectives: 17, 15, 14, 26, 9, 4, 19, 12, 9, 15
Calculate control limits for the no. of defective units.
Solution-: n = 400, k (No. of samples) = 10, Σd (total no. of defectives) = 140
nn = Σd/k = 140/10 = 14
Now, = nn /n = 14/400 = 0.035,
»q̅̅ = 1- ̅̅ = 1- 0.035 = 0.965
nn = 14 (central line)
UCL= nn + 3√ n√ q̅̅ LCL= nn - 3√ nn q
̅̅ = 14 + 3√400x0.035x0.965 = 14 - 3√400x0.035x0.965
= 25.025 = 2.975

## Slide 15: USES-:
The following are the field of application


of C-Chart-:
Number of defects of all kinds of aircraft final assembly.
Number of defects counted in a roll of coated paper, sheet of photographic film, bale of cloth etc.